Getting the build system components
Instead of wget you can use any download manager:
wget http://www.pengutronix.de/software/ptxdist/download/v1.99/ptxdist-1.99.2.tgz
wget http://www.pengutronix.de/software/ptxdist/download/v1.99/ptxdist-1.99.2-patches.tgz
svn co https://pdaxrom.svn.sourceforge.net/svnroot/pdaxrom/branches/pdaxrom-2.0/
svn co https://pdaxrom.svn.sourceforge.net/svnroot/pdaxrom/branches/pdaxrom-2.0-external-deps/
Build system installation
Unpack the archives:
tar xfz ptxdist-1.99.2.tgz
tar xfz ptxdist-1.99.2-patches.tgz
Install the additional packages required for work:
aptitude install libncurses5-dev libncurses5 gawk m4 bison flex expect gettext
Note: When building the package xorg-data-xkbdata.make for your target, it will require x11-xkb-utils to be installed on your host system. This can be installed by:
aptitude install x11-xkb-utils
Go to the work directory:
cd ptxdist-1.99.2
Configure the build system to install it to /opt/ptxdist (or any directory):
./configure –prefix=/opt/ptxdist
Compile and install the build system:
make
make install
Export the path to executable files:
export PATH=$PATH:/opt/ptxdist/bin
cd ..
You can use cross-development tools which are ready compiled or compile its yourself:
cd pdaxrom-2.0-external-deps/OSELAS.Toolchain-1.1.1
ptxdist select ptxconfigs/arm-v5te-linux-gnueabi_gcc-4.1.2_glibc-2.5_linux-2.6.18.ptxconfig
ptxdist go
At this point your Cross-Compiler Binaries are fully built

Target system configuration and build:
cd pdaXrom-2.0
Select the configuration:
ptxdist select boardconfigs/akita.light (C1000, C3100 and C3200 Shell Build no X)
/akita.full (C1000, C3100 and C3200 X Build)
/Corgi.light (C750,C760, C860 Shell Build no X)
Select the path to crosscompiler:
ptxdist toolchain /opt/OSELAS.Toolchain-1.1.1/arm-v5te-linux-gnueabi/gcc-4.1.2-glibc-2.5-kernel-2.6.18/bin/
If the configuration is needed to be edited perform the following command:
ptxdist menuconfig
Start to compile the target system:
ptxdist go
Build the file system image:
ptxdist images
The rootfs image and kernel will be placed in images directory, unpacked root file system in root directory and root file system with debug information in root-debug directory.

Testing and debuging in QEMU emulator
Install the emulator:
aptitude install qemu
The following configurations are available for compiling:
- qemuarm.light
- compiler - arm-v5te-linux-gnueabi_gcc-4.1.2_glibc-2.5_linux-2.6.18
- start the system in the emulator: qemu-system-arm -M versatilepb -kernel linuximage -hda root.ext2 -nographic -append "console=ttyAMA0 root=/dev/sda"
- qemux86.light
- compiler - i686-unknown-linux-gnu_gcc-4.1.2_glibc-2.5_linux-2.6.18
- start the system in the emulator: qemu -kernel linuximage -hda root.ext2 -append root=/dev/hda